Honda Motorcycle Part Codes

All parts on a Honda motorcycle have a unique part number. Honda divides parts into two broad categories, General Parts and Standard Parts. General parts are those unique to Honda, such as valves, pistons, gas tank etc. Standard parts are parts that follow universal standards, such as nuts, bolts and such.

General Parts

General parts have a part number divided into 3 sections, such as 22201-166-000 (clutch friction plate for the TL125).

- The first string of digits (22201-XXX-XXX) indicates the Honda function and component number for this part. For example, there are several different part numbers for the TL clutch friction plate, all sharing funtion/component number 22201. Clutch steel plates have f/c code 22311, indicating same function but different component.

- The second string of digits (XXXXX-166-XXX) is the product code, also known as Parts Classification Number in hondaspeak. This is the number that indicates the product (motorcycle) where this particular part was first used. See below for a complete listing of older Honda product codes. 166 indicates that the TL clutch friction plates where first used in Honda MB5 motorcycle. Honda often lists several different part numbers for the same part, indicating slight differences in the part, such as different supplier etc. For example there are four different part numbers listed for the clutch friction plates.

All TL125 models (1973 K, 1974 K1, 1975 K2 and 1976 S) share the product code 355. All General parts having a different product code are "recycled" from other Honda models. Only parts with code 355 were originally designed for the TL125, but may have been used in later Honda models. The product code is probably the most interesting portion of the part number when trying to determine interchangeability of Honda parts between various models.

- The third string of digits (XXXXX-XXX-000) is the Classification Number. I believe it is mostly used to indicate various suppliers or improvements for the same part. Also any potential color code is tacked at the end of the classification number as digits (letters) 4 & 5.

Note that some pretty universal parts are still listed under General Parts number. For example most (all?) TL oil seals carry a general parts number. Luckily Honda parts fiche lists the actual dimensions for parts like this.

Standard Parts

Standard Parts have a part number divided into 2 sections, such as 93500-06040 (6mm x 40mm pan screw, for example TL125 clutch side engine cover).

- The first string of digits indicates the function/type of the standard part, for example all pan screws are 93500-XXXXX.

- The second digit indicates dimensions for the part.

- Standard parts occasionally have a third string of digits indicating the ISO standard designation and chemical surface treatment.

Back to TL125 homepage

Honda Motorcycle Product Codes

Following is a list of Honda motorcycle product codes. They are directly from an article posted on the VJMC (Vintage Japanese Motorcycle Club) website, typed in by Ellis Holman. I don't update this list and looks like it is no longer available from the VJMC website.

Addition: Richard Pade has found a more comprehensive list at CMS (Classic Motorcycle Supply).

| Model | Product Code |  | Model | Product Code |  | Model | Product Code |
| --- | --- | --- | --- | --- | --- | --- | --- |
| C100 | 001 |  | CA100T | 001 |  | C105T | 002 |
| C102 | 003 |  | CA100 | 005 |  | CA102 | 006 |
| CA105T | 007 |  | C110 | 011 |  | CA110 | 022 |
| S90 | 028 |  | CA200 | 030 |  | CT200 | 033 |
| CT90K0 | 033 |  | CM91 | 034 |  | S65 | 035 |
| P50 | 044 |  | Z50AK0/K1/K2 | 045 |  | CL90/CL90L | 056 |
| PC50 | 063 |  | SL90 | 074 |  | CT90K1 | 077 |
| C70MK0 | 087 |  | CL70K0 | 089 |  | C70K1 | 092 |
| CT70HK0/K1 | 098 |  | CT70K0/K1/K2/K3/K4/ '76/'77/'78 | 098 |  | CT90K3/K4/K5/K6/ '76/'77/'78/'79 | 102 |
| CB100 K0/K1/K2 | 107 |  | CL100 K0/K1/K2/ S0/S2/S3 | 108 |  | SL100 K0/K1/K2/K3 | 110 |
| CL70K1/K2/K3 | 111 |  | QA50K0 | 114 |  | XR75 K0/K1/K2/ '76 | 116 |
| SL70K0 | 118 |  | SL70K1 | 118 |  | Z50AK3 | 120 |
| CT70 '79/'80/ '81/'82 | 126 |  | ST90 K0/K1/K2 | 128 |  | QA50K1/K2/K3 | 129 |
| Z50AK4/K5/K6/ 76/77/78 | 130 |  | MR50K0,K1 | 131 |  | XL70K0/K1/'76 | 137 |
| NC50,77/78/79/80 | 147 |  | PA50I&II | 148 |  | XL75 '77/'78/ '79 | 152 |
| XR75 '77/'78 | 153 |  | NA50,79/80 | 163 |  | MB5 | 166 |
| CR80R '80/'81 | 169 |  | C70 '80/'81 | 174 |  | XR80 '79/'80/'81 /'82/'83/'84 | 176 |
| Z50R,79/80/81/82/83 /84/85/86/86D/87 | 181 |  | NX50M, 81/82 | 187 |  | NA50 81 | 190 |
| NC50, 81 | 193 |  | XL80S '80/'81/'82/ '83/'84/'85 | 195 |  | CB500K2 | 323 |
| CA92 | 203 |  | CB92 | 205 |  | CA95 EARLY/LATE | 206 |
| CB160 | 217 |  | CL160/CL160D | 223 |  | CA160 | 225 |
| CB500 K0/K1 | 232 |  | CL175K0 | 236 |  | CA175/CD175 | 237 |
| CL125A | 243 |  | SS125A | 244 |  | CA71/C71 | 255 |
| CE71 | 257 |  | C72 | 259 |  | C76/CA76 | 260 |
| CS76/CSA76 | 261 |  | CA72 EARLY/LATE | 262 |  | C77 | 266 |
| CA77 EARLY/LATE /CSA77 | 267 |  | CB72 | 268 |  | CL72 | 273 |
| CB77 | 275 |  | TL250 K0/'76 | 376 |  | CL77 | 278 |
| CB450 K0 | 283 |  | CB350 K0/K1 | 287 |  | CL350 K0/K1 | 291 |
| CB450 K1/K2 | 292 |  | CB450D | 293 |  | CL450 K1/K2 | 294 |
| CB750 K0/K1 | 300 |  | CA175K3/CD175K3 | 302 |  | CB175K3 EARLY/LATE | 306 |
| CL175K3 | 307 |  | SL350 K0 | 310 |  | SL350 K1 | 312 |
| SL175 K0 | 313 |  | CB175 K4/K5 | 315 |  | CL175 K4/K5 | 316 |
| CB350 K2/K3/K4 | 317 |  | CL350 K2/K3 | 318 |  | CB450 K3/K4 | 319 |
| CL450 K3/K4 | 320 |  | CB125 S0/S1/S2 | 324 |  | MT125R '77/'78 | 325 |
| XL250 K0/K1/K2 | 329 |  | SL125 K0/K1/K2 | 331 |  | CB350 FOUR F0/F1 | 333 |
| SL175 K1 | 334 |  | SL350K2 | 340 |  | CB750 K2/K3/ K4/K5/'76 | 341 |
| CB175 K6 | 342 |  | CL175 K6 | 343 |  | CB350G | 344 |
| CL350 K4/K5 | 345 |  | CB450 K5/K6/K7 | 346 |  | CL450 K5/K6 | 347 |
| CB200 K0/T0 | 354 |  | TL125 K0/K1/K2/'76 | 355 |  | XL350 K0/K1 | 356 |
| CR250 M0 | 357 |  | MT250 K0/K1/'76 | 358 |  | CL125 S0/S1 | 359 |
| CR125 M0/M1 | 360 |  | MT125 K0/K1/'76 | 361 |  | XL175 K0/K1 | 362 |
| XL100 K0/K1/'76/'77/'78 | 364 |  | XL125 K0/K1 | 365 |  | CB360 K0/CB360G/ CB360T/CB360T '76 | 369 |
| CL360 K0/K1 | 370 |  | GL1000 K0/'76/LTD '76/'77/ | 371 |  | MR175 K0/'76/'77 | 373 |
| CB550 FOUR K0/K1/'76 | 374 |  | CB500T | 375 |  | CB400 FOUR F0/'76/'77 | 377 |
| CL200 | 378 |  | CR250 M1/M2 | 381 |  | XL125 '76/'77/'78 | 382 |
| CB125S '76/'77/'78/'79/80/'81/'82 | 383 |  | XL350 '76/'77/'78 | 385 |  | XL250 '76/ | 386 |
| CJ360T '76/'77 | 388 |  | CB200T '76 | 389 |  | CB550F F0/'76/'77 | 390 |
| XL175 '76/'77/'78 | 391 |  | CB750F F0/'76 | 392 |  | CB750A '76/'77/'78 | 393 |
| MR250 | 395 |  | CR125 M'76/M'77/M'78 | 400 |  | CT125 '77 | 401 |
| CB550K '77/'78 | 404 |  | CB750 '77/'78 | 405 |  | CB750F '77/'78 | 410 |
| CB400TI '78/'79/CB400TII '78/'79/CB400T '80/'81 | 413 |  | CX500 '78/'79 | 415 |  | CB400A '78 | 417 |
| CM185t '78/'79 | 419 |  | CBX '79 | 422 |  | CB750C '80 | 425 |
| CB750K '79/'80 | 425 |  | CB650 '79 | 426 |  | XL185S '79/'80/'81/'82 | 427 |
| XL250S '78/'79/'80/'81 | 428 |  | XR500 '79/'80 | 429 |  | CR250R '78/'79 | 430 |
| GL1000 '78/'79 | 431 |  | XR250 '79/'80 | 434 |  | XL500S '79/'80/'81 | 435 |
| XL100 '79/'80/'81 | 436 |  | XL125S '79/'80/'81 | 437 |  | CB900F '81 | 438 |
| CB125S '84/'85 | 441 |  | CR125R '79 | 444 |  | CB750F '79/'80/'81 | 445 |
| XR185 '79 | 446 |  | XR200 '80/'81/'82/'83/'84 | 446 |  | CM400C '81/CM400E '80 | 447 |
| CM400E '81/CM400T '79/CM400T '80/'81 | 447 |  | CM400A '79/'80/'81 | 448 |  | CX500C '79/'80/'81/82 | 449 |
| CB175K7 | 453 |  | CL175 K7 | 454 |  | CT110 '80/'81/'82/'83/'84/'85/'86 | 459 |
| CB650 '80/'81/'82 CB650C '81 CB650SC '82 | 460 |  | CB700C '80/'81/'82 | 461 |  | GL1100 '80/'81 | 463 |
| GL1100I '80/'81 | 463 |  | CM200T '80/'81/'82 | 465 |  | CR125R '80 | 466 |
| CR250R '80 | 467 |  | CBX '80 | 469 |  | CX500D '79/'80/'81 | 470 |
| NC50, 82/83 | GA6 |  | C70 '82/'83 | GB5 |  | PA50II, 81/82/83 | GB7 |
| NU50, 82/83 | GC1 |  | NU50M, 82/83 | GC1 |  | CR80R '82/'83/'84/'85/'86 | GC4 |
| CR60R '83/'84 | GF5 |  | XR80 '85/'86/'87/'88 | GN1 |  | CR80R '87/'88 | GS2 |
| ZB50 88 | GS9 |  | Z50R 88 | GW8 |  | TR200 '86/'87 | HB7 |
| XR200R '81/'82/'83 | KA2 |  | CR125R '81/'82/'83/'84/'85 | KA3 |  | CR250R '81/'82/'83/'84/'85 | KA4 |
| CR450R '81/ CR480 '82/'83 | KA5 |  | CR500R '84/'85 | KA5 |  | XR250R '81/'82 | KA6 |
| XL100S '82/'83/'84/'85 | KA8 |  | XR100 '81/'82/'83/'84 | KA9 |  | XL125S '82/'84/'85 | KB1 |
| CM250C '82/'83 | KB4 |  | XL250R '82/'83 | KB7 |  | XR350R '83/'84 | KF0 |
| XL185S '83 | KF9 |  | XL200R '83/'84 | KG1 |  | TLR200 '86/'87 | KJ2 |
| XR200R '84/'85 | KK0 |  | XR250R '84/'85 | KK1 |  | XL350R '84/'85 | KL3 |
| XL250R '84/'85 | KL4 |  | XR100R '85/'86/'87/'88 | KN4 |  | XR350R '85 | KN5 |
| CMX250C '85/'86/'87 CMX250CD '86 | KR3 |  | CR125R '86/'87/'88 | KS6 |  | CR250R '86/'87/'88 | KS7 |
| XR200R '86/'87/'88 | KT0 |  | XR250R '86/'87/'88 | KT1 |  | XL250R '86/'87 | KT4 |
| VTR250 '88 | KV0 |  | NX250 '88 | KW3 |  | NX125 '88 | KY7 |
| XR500R '81/'82 | MA0 |  | GL500 '81/'82/'81/'82 INTERSTATE | MA1 |  | CBX '81/'82 | MA2 |
| CB750K '81/'82 | MA4 |  | CB750C '81/'82 | MA5 |  | VF700S '84/'85 | MB0 |
| VF750S '82/'83 | MB0 |  | VF750C '82/'83 | MB1 |  | VF700C '84 | MB1 |
| VF700F '84/'85 | MB2 |  | VF750F '83/'84 | MB2 |  | VF1100S '84/85 | MB3 |
| VF1100C '83/'84/'85/'86 | MB4 |  | VF100F '84 | MB6 |  | CB900F '82 | MB7 |
| GL1100 '82/'83 GL1100A '82/'83 GL1100I '82/'83 | MB9 |  | CM450C '82 | MC0 |  | CM450A '82/'83 | MC1 |
| CM250E '82/'83 | MC2 |  | CB750F '82 | MC3 |  | XL500R '82 | MC4 |
| CX500TC | MC7 |  | VT500FT '83 | MC8 |  | FT500 '82/'83 | MC8 |
| CB450SC '82/'83/'85/'86 | MC9 |  | CB450T '82 | ME0 |  | CB750SC '82/'83 | ME1 |
| CL650 '83 / CL650I '83 | ME2 |  | CB550SC '83 | ME4 |  | CB650SC '83/'84/'85 | ME5 |
| CX650T '83 | ME7 |  | CX650C '83 | ME8 |  | VT700C '84/'85 | ME9 |
| VT750C '83 | ME9 |  | VF500F '84/'85 | MF2 |  | VT500C '83/'84/'85/'86 | MF5 |
| VT500FT '84 | MF8 |  | CB1000C '83 | MG1 |  | XL600R '83/'84/'85 | MG2 |
| XR500R '83/'84 | MG3 |  | CB1100F '83 | MG5 |  | VT1100C '85/'86 | MG8 |
| GL1200 '84/GL1200A '84/GL1200A '85 | MG9 |  | GL1200L '85 | MG9 |  | GL1200I '84/'85 | MG9 |
| CB700SC '84/'85/'86 | MJ1 |  | VF1000R '85/'86 | MJ4 |  | VF500C '84/'85 | MJ8 |
| XR600R '85/'86/'87 | MK2 |  | VF700C '85/'86 | MK3 |  | VT700C '86/'87 | MK7 |
| VFR700F '86/VFR700F2 '86/VFR700F2 '87 | MK8 |  | CR500R '86/'87/'88 | ML3 |  | XL600R '86/'87 | ML6 |
| VFR750F '86 | ML7 |  | GL1200A '86/'87 | ML8 |  | GL1200SE-i '86 | ML8 |
| GL1200I '86/'87 | ML8 |  | VF500F '86 | MM1 |  | CMX450C '86/'87 | MM2 |
| CBR1000F '88 | MM5 |  | VT1100C '87/'88 | MM8 |  | VF700C '87 | MN0 |
| XR600R '88 | MN1 |  | VF750C '88 | MN2 |  | CBR600F '87/'88 | MN4 |
| GL1500 '88 | MN5 |  | CBR1000F '87 | MN5 |  | NT650 '88 | MN8 |
| NX650 '88 | MN9 |  | VT600C '88 | MR1 |  | VT800C '88 | MR6 |

If you find anything you want to comment or add, please go to the Honda TL125 Feedback Page.

Back to TL125 homepage

| This page maintained by Jarmo Kaila Last modification December 14, 2003 |  |
| --- | --- |

Honda Motorcycle Part Codes